# LOOP® Type 2

The LOOP® system is an open metal ceiling with a free cross-section of more than 50 %. Due to its flare with a height of 5 mm, the hole pattern consisting of offset rows [RV-50-40] has a 3-dimensional visual effect and hides the ceiling cavity very well. The S-shaped edges of the ceiling elements are made by bypassing the perforation, thus interlocking both the longitudinal and front-side joint. The elements are screwed to the suspension substructure with a small join, which allows small tolerances in both the x and y directions.

The suspension substructure consists of a form-punched primary carrier [U1040] as lateral grid, which is suspended from the raw ceiling with Nonius upper and lower parts or with threaded rods using officially approved dowel plugs. The primary carriers are to be connected together at the ends by means of longitudinal connectors [U 1041] [screw fasteners]. The spacing of the primary carriers is according to the requirements of DIN EN 13964 as well as the loads of the system and is to be determined and checked by the contractor. The primary carriers are attached to the walls with U 1042 wall brackets. Using the primary carrier module adapters [U 1043], the C-profiles [C41-LOOP®] are mounted as longitudinal profiles to the primary carriers. Longitudinal connection of the C-profiles is via the longitudinal connectors [C41-LVB]. LOOP® adapters [75 LOOP® adapter] are threaded on the C-profiles and the LOOP® elements are attached to the adapters using counter-sunk screws. The Loop standard module is available in the module dimensions 966 x 1115.44 mm. Only those constructional components may be used which are approved by the manufacturer.

Acoustics

To improve sound absorption, the LOOP® elements can be lined with a perforated steel sheet with a fleece. The lining can be provided with a choice of colors [powder-coated similar to RAL …].

Integration artificial light

The LOOP® roundings are suitable for the integration of the built-in LED-based PUNTEO®-J luminaire which can be integrated in the LOOP® elements, i.e. a separate suspension is usually not required. All luminaires have a flexible connection and can be removed together with the ceiling plate. The ballast units are located in the ceiling void. The PUNTEO®-J units can be positioned freely within the LOOP® elements via adapters.

Leading brand system durlum System LOOP® with Punteo-J® or equivalent. Consisting of:

| Pos............................ ..............................m2 | Delivery and installation of LOOP® ceiling elements, Material: Aluminium, t = 2 mm Surface: optional: ( DUROPLAN® A050 or ( powder-coated similar to RAL … Length of module: 966 mm Width of module: 1115.44 mm Unit price: … €/m² Total price: … € |
| --- | --- |
| Pos............................ ..............................m2 | Delivery and installation of LOOP® ceiling elements with integrated built-in PUNTEO®-J luminaires Material: aluminium; t=2 mm with stiffeners, silver anodized Surface: optional: ( anodized DUROPLAN® A050 or ( powder-coated similar to RAL … Length of module: 966 mm Width of module: 1115.44 mm … pcs. PUTNEO®-J and PUTNEO®-J adapter each Optional: ( PUN J085-018N3-01 [warm white/3000 K] or  PUN J085-018N4-01 [neutral white/4000 K] Connected load: 20 W with transformer Luminous flux: LED 3000 K/4000 K: 2157 lm/ 2255 m Fitted with: 18 W LED array replaceable System efficiency: max. 82 lm/W Lighting technology: narrow beam – 2 x 20 ° Material: installation ring, aluminium precision-turned; reflector, aluminium anodized Installation height: min. 135 mm Ceiling opening: Ø 74 mm Incl. LED driver Dali dimmable: LVG 500-024-02-02 incl. PUN J 085-018-Z 001 PUTNEO®-J adapter Unit price: … €/m² Total price: … € |
| Pos............................ ............................Pcs | Set-up charge per format, version and call-off |
| Pos............................ ..............................m2 | Delivery and installation of a suspension system for LOOP® system Form-punched primary carriers [U1040] as lateral grid, black Longitudinal frame connectors [U 1041] for primary carriers at the ends Wall brackets [U 1042] C-profile [C41-LOOP®] black C-profile [C41-LVB] connector Primary carrier module adapter [U 1043] LOOP® adapter [75 LOOP® adapter ] Nonius upper and lower parts Color-matched counter-sunk screws for LOOP® Unit price: … €/m² Total price: … € |