# Open Sky |  Translucent glass ceiling

The system consists of hinged glass elements and requires no tools. A junction point construction connects the elements to the substructure of the design. Glass sizes of B: 500…1200 mm and L: 500…1200 mm are available and are sealed all around with an 8 mm seam. The glass is heat-strengthened and a translucent film connects all panes. All edges are polished and chamfered. The design is perfectly suited for glass ceilings.

The junction points are attached to a wide-span girder system, consisting of a primary and of a secondary profile so that every position in a room can be reached [see detail 1]. Single, double, triple and quadruple arm junction points can be supplied. These facilitate a range of spatial options, which may even include triangular or trapezium-shaped glass surfaces. The contractor develops the reflected ceiling plan.

The junctions are equipped with a pivot joint and a lock component. The opening mechanism is released by slightly pressing against the glass pane. This glass pane is fitted with a safety chain and cushioning mechanism to prevent the pane from swinging down. An elastic coupling element with stainless steel head connects the pane and the hinge/locking device.

If necessary, the contractor may be required to provide static calculations for the constructions. The total height from the bottom edge of the glass pane up to the top edge of the wide-span girder amounts to approx. ~365 mm (and/or. ~510 mm up to the top edge of the reflector in order to achieve an even distribution of light).

The lighting system will be mounted above the wide-span girder to only indirectly illuminate the glass elements. An even illumination of the glass elements is achieved by the use of highly reflective wide angle reflectors. Per running meter glass pane, 1 rm of linear lighting will be required.

Lighting system:	with adjustable ECGs.

Wall connection:	Generally, a gypsum board or a hinged metal panel or a suspension hook system (durlum system S4) or durlum profile types are used to frame the array of translucent glass ceiling panels.

Translucent glass ceiling system durlum Open Sky or similar, consisting of:

| Pos. running m | Delivery and mounting of an Open Sky subconstruction consisting of wide-girder profiles [rough and fine grid], comprised of a galvanized 40/40/3 mm profile. Attachment of the profiles to each junction point using a cross connector and a special screw. The profile grid will be suspended using M12 threaded rods [in acc. with detail 2] and an approved mounting plug [load introduction acc. to structural calculations]. Subconstruction within the planning grid … mm x … mm in accordance with the above description, the reflected ceiling plan and the static requirements and to the mounting instructions of the manufacturer. Single, double, triple and quadruple arm junction points can be attached to every junction point. Price per unit: … €/rm TP: … € |
| --- | --- |
| Pos. pcs. | Quadruple junction points, consisting of a fixing sheet, four bars, two pivoting joints and two Durloc lock elements with safety rope. Delivery and mounting. Price per unit: … €/pcs. TP: … € |
| Pos. pcs. | Triangular junction points, consisting of a fixing sheet, three bars, two pivoting joints and two Durloc lock elements with safety rope. Delivery and mounting. Price per unit: … €/pcs. TP: … € |
| Pos. pcs. | Double junction points, consisting of a fixing sheet, two bars, two pivoting joints and two Durloc lock elements with safety rope. Delivery and mounting. Price per unit: … €/pcs. TP: … € |
| Pos. pcs. | Single junction points, consisting of a fixing sheet, one bar, optional with pivoting joints or Durloc lock elements with safety rope [see ceiling plan]. Delivery and mounting. Price per unit: … €/pcs. TP: … € |
| Pos. pcs. | TVG glass pane with polished edges L = approx. … mm W = approx. … mm With respectively four and/or three, two or one boreholes with integrated lock element and/or hinged element [depending on the supplied reflected ceiling plan]. Delivery and mounting. Price per unit: … €/pcs. TP: … € |
| Pos. pcs. | As with the position above but as triangle Delivery and mounting. Price per unit: … €/pcs. TP: … € |
| Pos. pcs. | As with the position above but as trapeze Delivery and mounting. Price per unit: … €/pcs. TP: … € |
| Pos. running m | Linear lighting attached to wide-span girder – rm in accordance with the panes' spacing. Delivery and mounting. Price per unit: … /rm TP: … € |